## Slide 1
Closetline® Packaged Heat Pumps

## Slide 2: Closetline® Heat Pumps

## Slide 3: Product line overview

## Slide 4: Closetline® WC Compact Series
Capacity - 11 sizes: 0.5 to 5-ton
5 Voltages Available –
  208-230/60/1
  265/60/1
  208-230/60/3
  460/60/3
  575/60/3
Compact Footprint
Single-stage operation

## Slide 5: Closetline® WC Compact – EC Motor ratings

## Slide 6: Closetline® WC Compact Series
Standard or Deluxe solid state control board
PSC or EC fan motors (high-static PSC motors are being phased-out)
Refrigerant Detection System (RDS)
  Optional sizes 4 ton & below
  Required sizes 5 ton & above
All valves are field installed in the hose kit.

## Slide 7: Closetline® WC Compact Series Options
High efficiency ECM CV & CT motors blower motors
Deluxe solid-state controls
DDC Control board (BACnet, Modbus, and JCI N2)
Cupro-nickel water heat exchanger
Enhanced low sound package
Tin-plated air coils for added protection from formicary corrosion
Stainless-steel drain pans
Extended-range for geothermal applications
Electrical service disconnect

## Slide 8: Closetline® WR Mid-Size Series
Capacity - 11 sizes: 0.5 to 5-ton
6 Voltages Available –
  115-1-60
  208-230/60/1
  265/60/1
  208-230/60/3
  460/60/3
  575/60/3
Mid-Size Cabinet Footprint
Single-stage operation

## Slide 9: Closetline® WR Mid-Size – EC Motor ratings

## Slide 10: Closetline® WR Mid-Size Series
Standard or Deluxe solid state control board
PSC or EC fan motors (high-static PSC motors are being phased-out)
Refrigerant Detection System (RDS)
  Optional sizes 4 ton & below
  Required sizes 5 ton & above
Factory installed water options are available.

## Slide 11: Closetline® WR Mid-Size Series Options
High efficiency ECM CV & CT motors blower motors
Deluxe solid-state controls
DDC Control board (BACnet, Modbus, and JCI N2)
Hybrid hydronic heating
Cupro-nickel water heat exchanger
Enhanced low sound package
Tin-plated air coils for added protection from formicary corrosion
Hot water generator
Internal circulators
Autoflow regulators
Motorized water valves
Stainless-steel drain pans
Internal electrical disconnect
Extended-range for geothermal applications
Electrical service disconnect
Waterside economizers

## Slide 12: Closetline® WZ 2-Stage Mid-Size Series
Capacity - 6 sizes: 2 to 5-ton
3 Voltages Available –
  208-230/60/1
  208-230/60/3
  460/60/3
Mid-Size Cabinet Footprint
Two-stage operation

## Slide 13: Closetline® WZ 2-Stage – EC Motor ratings

## Slide 14: Closetline® WZ 2-Stage Mid-Size Series
Deluxe solid state control board
EC-CV fan motors
Refrigerant Detection System (RDS)
  Optional sizes 4 ton & below
  Required sizes 5 ton & above
Factory installed water options are available.

## Slide 15: Closetline® WZ 2-Stage Mid-Size Series Options
DDC Control board (BACnet, Modbus, and JCI N2)
Hybrid hydronic heating
Cupro-nickel water heat exchanger
Enhanced low sound package
Tin-plated air coils for added protection from formicary corrosion
Hot water generator
On/off internal circulators
Variable speed Internal pumps
Modulating water valves
Internal electrical disconnect
Extended-range for geothermal applications
Electrical service disconnect

## Slide 16: Standard Solid-State Control
Standard Control
Inputs:
  Digital – 10
  Analog – 7
Outputs:
  Digital – 6
  Analog – 1
Communications: 2
  RS-485 (Modbus)
  Serial
Aux Elec Heat
Safeties:
HP, LP, FP1, FP2
CO
Compressor
Loop Pump Options
Variable speed pump (PWM)
Modulating valve (0-10V)
24VAC Thermostat
Alarm Relay
Diagnostics Sensors
(EWT, LWT, LAT, CDT)
Modbus Comms
On-board Fuse - CE
ECM Constant Torque
PSC (Single Stage)
Add On Port:
Analog Outputs
uArt, SPI
Comms (LIN Bus)
Test Mode Button
Fault / Status LEDs
DIP Switch Bank

## Slide 17: Control Safeties
Anti-short cycle time delay on compressor operation.
Low voltage protection.
High voltage protection.
Condensate overflow electronic protection.
Water coil low temperature sensing (selectable for water or anti-freeze).
Air coil low temperature sensing.
Entering and leaving water temperature sensing.
Compressor discharge temperature sensing.

## Slide 18: Control Safeties
Emergency shutdown contacts.
Random start on power up mode.
Option to reset unit at thermostat or disconnect.
Automatic intelligent reset. Unit automatically resets 5 minutes after trip if the fault has cleared. If a fault occurs three times sequentially without thermostat meeting temperature, then lockout requiring manual reset will occur.
Ability to defeat time delays for servicing.
The low-pressure switch is not be monitored for the first 120 seconds after a compressor start command to prevent nuisance safety trips.
24V output to cycle a motorized water valve or other device with compressor contactor.

## Slide 19: Deluxe Solid-State Control
Deluxe Control
Inputs:
  Digital – 13
  Analog – 8
Outputs:
  Digital – 10
  Analog – 2
Communications: 2
  RS-485 (Modbus)
  ClimateTalk (Emerson)
Modbus Comms
Diagnostics Sensors
(EWT, LWT, LAT, CDT)
On-board Fuse - CE
VFD Blower
Loop Flow Options
Variable speed pump (PWM)
Modulating valve (0-10V)
Dehumidification pump
Aux Elec Heat
Accessory Relays:
*Cycle with Fan
OA Damper
Water Valve
WSE
Digital NSB
Dehumidification
*Cycle with Compressor
Humidifier
Constant Volume ECM
ECM Constant Torque
PSC (Single Spd; 2-Spd)
Safeties:
HP, LP, LT1, LT2
CO
24VAC Thermostat
2nd Stage Compressor
1st Stg Compressor
Alarm Relay
Test Mode Button
Fault / Status LEDs
HWG
DIP Switch Banks

## Slide 20: Deluxe control features
Same safeties as the standard control plus….
Boilerless system heat control at low loop water temperature.
Ability to allow up to three units to be controlled by one thermostat.
Relay to operate an external damper.
Relay to start system pump.
75VA control transformer. Control transformer shall have load side short circuit and overload protection via a built-in circuit breaker.

## Slide 21: Solid-State Control Comparison

## Slide 22: Minimum Installation Area – WC/WR/WZ 060
Minimum area where a blower-equipped unit must be installed, and mechanical / natural ventilation is not required

## Slide 23: Refrigerant Detection System
Upon leak detection the system shuts down compressor operation & runs the fan to disperse any concentration of leaked refrigerant
RDS Includes:
  2 sensors per board​
  Sensor connector is unique​
  Multiple power supply for redundancy
  No field adjustments or calibration during 15+ year life
Sensors

## Slide 24: Horizontal Unit Dimension Comparison

## Slide 25: Vertical Unit Dimension Comparison

## Slide 26
Questions?
Notes: 26