## Slide 1
Innoline® Riser Fan Coil Units &
Innoline® 50/50 4-Pipe System

## Slide 2: Innoline® Riser Fan Coil
What is an Innoline® Riser Fan Coil?
The product that started The Whalen Company
It’s a valveless fan coil
The risers are inside the cabinet with fins on them
One of if not the smallest footprint unit on the market

## Slide 3: Innoline® Riser Fan Coil
What is an Innoline® Riser Fan Coil?
A different type of fan coil than anyone else
A tremendous opportunity for replacement for those markets with an installed base.
A tremendous opportunity for those owners that are looking for operating savings.

## Slide 4: Innoline® Riser Fan Coil
Whalen Innoline® 2-Pipe Heat Only vs. Baseboard heating
Same finned tube type coil
Enclosed in a cabinet with a forced air fan
Very simple & Very reliable forced air, finned tube, radiator
All solder joints are external to the cabinet

## Slide 5: Ideal Buyer
More often than not, it will be the building owner that is planning to operate the building long term.
Unit longevity, efficiency, and low maintenance are the drivers

## Slide 6: Innoline® Riser Fan Coil
200 to 800 CFM
Footprint
  200 to 300 CFM: 12” x 14”
  400 to 500 CFM: 16” x 14”
  600 to 800 CFM: 18” x 16”
Smallest footprint on the market
Lower Pumping Costs: Elimination of system resistance caused by system valves, coils, and run-out piping
Add the Innoflow™ valve to take advantage
of a Variable Flow System
Full time humidity control: Face and Bypass Dampers
Unit types
  2-Pipe Riser Fan Coil
  4-Pipe Riser Fan Coil
  Whalen Heater

## Slide 7: The Whalen System
It works by Thermodynamic Performance
Average water temperature
  Total riser GPM goes through each unit
  Takes advantage of a large finned surface area
Primary and secondary surface
Four air passes
Humidity control

## Slide 8: The Whalen System
Average water temp = 50ºF
(55.0 + 45.0)/2 = 50
(53.3 + 46.7)/2 = 50
(51.7 + 48.3)/2 = 50
(50.0 + 50.0)/2 = 50
45.0 EWT

## Slide 9: Unit Looping – Series Piping

## Slide 10: Unit Looping – Series Piping

## Slide 11: Innoline® Riser Fan Coil – Air Path

## Slide 12: Compact Riser Grouping
Supply
Return
Drain
Drain

## Slide 13: Riser Terminations
Top U-Bend with manual vent
Bottom U-Bend with drain valve
Bottom U-Bend

## Slide 14: The Whalen Concept
Condensate Drain

## Slide 15: Conditioning Outdoor Air

## Slide 16
Questions?
Notes: 16